## Slide 1: Praktijk Emails beheren:
This post aims to someone that is starting with Python but also can be useful to knowledgeable users who haven’t worked with email before. The version of Python used to make this post was 3.6.x.
The email Protocols
Email systems are robust because they rely upon well-established protocols used by all email platforms across the internet. These protocols are defined and published by documents called RFC that stands for Request for Comments and resemble the PEPs from Python, but for protocols and patterns that define the operation of communication systems through the internet.
To send emails, we use the SMTP protocol (RFCs 821 e 5321), and to receive them, we use IMAP (RFC 3501) or POP (RFCs 918 e 1081) protocols.
Sending emails
Simple Mail Transfer Protocol or SMTP is a protocol from the application layer used to send emails. It operates over TCP/IP, and your communication is often made using the port 25 or 587 for unencrypted connections and 465 for TLS/SSL encrypted connections.
Python comes with batteries included, so we don’t need to install any external package to deal with SMTP. We use a library called smtplib:
import smtplib from email.mime.text import MIMEText
connect with Google’s servers smtp_ssl_host = ‘smtp.gmail.com’ smtp_ssl_port = 465
use username or email to log in
username = ‘origin@gmail.com’ password = ‘password’
from_addr = ‘origin@gmail.com’ to_addrs = [‘destiny@gmail.com’]
the email lib has a lot of templates for different message formats, on our case we will use MIMEText to send only text
message = MIMEText(‘Hello World’) message[‘subject’] = ‘Hello’ message[‘from’] = from_addr message[‘to’] = ‘,’.join(to_addrs)
we’ll connect using SSL
server = smtplib.SMTP_SSL(smtp_ssl_host, smtp_ssl_port)
to interact with the server, first we log in and then we send the message
server.login(username, password) server.sendmail(from_addr, to_addrs, message.as_string()) server.quit()
In case you have problems to connect at Google, you need to enable the “Less secure app access”.
Google blocks access from apps that it judges as not following its security standards, the problem is they don’t have a clear explanation of what these standards are, besides that it’s not a trivial task for whom is starting and doing the first test to struggle with that.
That said if you are facing this issue, you can enable access to make your tests by accessing https://myaccount.google.com/u/0/security?hl=en
Now we can use Google as our gateway to send the messages, but keep in mind that even with Google as your gateway there is a policy of email sending, so be careful with SPAMS.
Receiving emails
The IMAP Internet Message Access Protocol is used to receive emails, and as on SMTP it operates at the application layer over TCP/IP. The port used for its connections is 143 for unencrypted and 993 for encrypted.
Another protocol that works for this task is POP Post Office Protocol, but IMAP is better due to its synchronization between the client and the server and also the ability to access more than the email inbox.
The process of receiving emails is more complicated than sending because you also have to search for the message and decode it:
import email import imaplib EMAIL = 'mymail@mail.com' PASSWORD = 'password' SERVER = 'imap.gmail.com' # connect to the server and go to its inbox mail = imaplib.IMAP4_SSL(SERVER) mail.login(EMAIL, PASSWORD) # we choose the inbox but you can select others mail.select('inbox') # we'll search using the ALL criteria to retrieve # every message inside the inbox # it will return with its status and a list of ids status, data = mail.search(None, 'ALL') # the list returned is a list of bytes separated # by white spaces on this format: [b'1 2 3', b'4 5 6'] # so, to separate it first we create an empty list mail_ids = [] # then we go through the list splitting its blocks # of bytes and appending to the mail_ids list for block in data: # the split function called without parameter # transforms the text or bytes into a list using # as separator the white spaces: # b'1 2 3'.split() => [b'1', b'2', b'3'] mail_ids += block.split() # now for every id we'll fetch the email # to extract its content for i in mail_ids: # the fetch function fetch the email given its id # and format that you want the message to be status, data = mail.fetch(i, '(RFC822)') # the content data at the '(RFC822)' format comes on # a list with a tuple with header, content, and the closing # byte b')' for response_part in data: # so if its a tuple... if isinstance(response_part, tuple): # we go for the content at its second element # skipping the header at the first and the closing # at the third message = email.message_from_bytes(response_part[1]) # with the content we can extract the info about # who sent the message and its subject mail_from = message['from'] mail_subject = message['subject'] # then for the text we have a little more work to do # because it can be in plain text or multipart # if its not plain text we need to separate the message # from its annexes to get the text if message.is_multipart(): mail_content = '' # on multipart we have the text message and # another things like annex, and html version # of the message, in that case we loop through # the email payload for part in message.get_payload(): # if the content type is text/plain # we extract it if part.get_content_type() == 'text/plain': mail_content += part.get_payload() else: # if the message isn't multipart, just extract it mail_content = message.get_payload() # and then let's show its result print(f'From: {mail_from}') print(f'Subject: {mail_subject}') print(f'Content: {mail_content}')
On this code, we extracted only the plain text of the email, but there’s much more you can extract, like the HTML content and the annexed files, but this can be a topic for a next post.
BONUS: Automate the cleaning of bloated mailboxes
Recently, my mailbox got bloated, and I had to do a clean up to get some space, but the high amount of messages overloaded the Gmail interface.
So, to solve that, and also for automating this tedious manual task, I wrote this:
import imaplib # caso sua caixa de emails esteja muito cheia # use esta variável para aumentar o limite do # tamanho da resposta imaplib._MAXLINE = 1000000 EMAIL = 'mymail@gmail.com' PASSWORD = 'password' SERVER = 'imap.gmail.com' mail = imaplib.IMAP4_SSL(SERVER) mail.login(EMAIL, PASSWORD) # select the box you want to clean mail.select('bloated_box') status, search_data = mail.search(None, 'ALL') mail_ids = [] for block in search_data: mail_ids += block.split() # define the range for the operation start = mail_ids[0].decode() end = mail_ids[-1].decode() # move the emails to the trash # this step is Gmail specific because # it doesn't allow excluding messages # outside the trash mail.store(f'{start}:{end}'.encode(), '+X-GM-LABELS', '\\Trash') # access the Gmail trash mail.select('[Gmail]/Trash') # mark the emails to be deleted mail.store("1:*", '+FLAGS', '\\Deleted') # remove permanently the emails mail.expunge() # close the mailboxes mail.close() # close the connection mail.logout()
import smtplib from email.mime.text import MIMEText # connect with Google's servers smtp_ssl_host = 'smtp.gmail.com' smtp_ssl_port = 465 # use username or email to log in username = 'origin@gmail.com' password = 'password' from_addr = 'origin@gmail.com' to_addrs = ['destiny@gmail.com'] # the email lib has a lot of templates # for different message formats, # on our case we will use MIMEText # to send only text message = MIMEText('Hello World') message['subject'] = 'Hello' message['from'] = from_addr message['to'] = ', '.join(to_addrs) # we'll connect using SSL server = smtplib.SMTP_SSL(smtp_ssl_host, smtp_ssl_port) # to interact with the server, first we log in # and then we send the message server.login(username, password) server.sendmail(from_addr, to_addrs, message.as_string()) server.quit()